## Slide 1: Communication Subsystem
By Ei Phyu Phyu

## Slide 2: Outline
Function and Performance Evaluations
Product Breakdown Structure – WBS
Communication Links
Communication RAS (System and Design Requirements)
Schedule

## Slide 3
S/N | Function | Perfomance Evaluations
1 | Receive uplink command from GS (Ground Station), and send the received command to OBC (On Board Computer) | UHF dipole antenna to receive 435 MHz uplink command.
 |  | Transceiver to receive and demodulate the uplink command in GMSK 4800 bps rate, and AX.25 frame format.
 |  | COMM MCU to send the command to OBC through UART.
2 | Receive the Telemetry/HK data from OBC, and transmit the Telemetry/HK data to GS. | COMM MCU to receive telemetry/HK data from OBC.
 |  | Transceiver to do GMSK modulation 4800 bps rate, and AX.25 frame format to Telemetry data.
 |  | Transceiver to process CW that contains HK data.
 |  | UHF dipole antenna to transmit Telemetry/HK data using 437 MHz downlink frequency
3 | Receive the payload data (SF packets) from OBC and transmit data to GS. | COMM MCU to receive payload data from OBC.
 |  | Transceiver to do GMSK modulation 4800 bps rate, and AX.25 frame format to payload data.
 |  | UHF dipole antenna to transmit Telemetry/HK data using 437 MHz downlink frequency.

## Slide 4: WBS
UHF Transceiver
1.1.1.3.1
UHF TX
1.1.1.3.1.1
COM
1.1.1.3
COM MCU 1.1.1.3.2
Modulator
1.1.1.3.1.2
UHF RX
1.1.1.3.1.3
Demodulator
1.1.1.3.1.4
Antenna
1.1.1.3.4
Antenna deployment unit
1.1.1.3.5
TX/RX Antenna
1.1.1.3.4.1
Fishing Wire
1.1.1.3.5.2
Burner Circuit
1.1.1.3.5.1
CW TX
1.1.1.3.1.5
COM FM 1.1.1.3.3

## Slide 5: Communication Links
 | Uplink (Receive Mode) | Downlink (Transmit Mode) | Beacon (CW Mode)
Frequency | 435 MHz | 437.375 MHz | 437.375 MHz
Bandwidth | 26 kHz | 26 kHz | 500 Hz
Modulation | GMSK | GMSK | CW Morse Code
Output Power | (GS) | 800mW (29.03 dBm) | 100mW (20 dBm)
Rate | 4800 bps | 4800 bps | 20 wpm

## Slide 6: Communication RAS
S/N | System requirement | S/N | Design Requirements | S/N | Verification Requirements | Verification Method
SR 1.1. | Satellite shall be able to receive uplink command from ground station. | DR 1.1.1 | Antenna shall be dipole that receives uplink command at 435 MHz. | VR 1.1.1.1 | Get the S11 parameter of the antenna. | Use simulation tool (e.g. CST, HFSS). Use Vector Network Analyzer (VNA) at anechoic chamber test.
 |  |  |  | VR 1.1.1.2 | Measure received signal power at the antenna. | Use Spectrum Analyzer (SA) at anechoic chamber test. Use SA at Long Range Test (LRT).
 |  | DR 1.1.2 | Modulation shall be GMSK at 4800 bps data rate. | VR 1.1.2.1 | Confirm the output waveform at the transceiver (TRX). | Use oscilloscope to check the waveform.
 |  | DR 1.1.3 | Frame format shall be AX.25 Protocol. | VR 1.1.3.1 | Determine the packet error. | Send pre-defined data and inspect the received data for errors.
 |  | DR 1.1.4 | COM MCU shall send the command to OBC through UART. | VR 1.1.4.1 | Check UART communication between COMM MCU and OBC. | Compare COMM MCU transmit data and OBC received data.
 |  |  |  | VR 1.1.4.2 | Conduct uplink success rate test. | Count packets successfully received vs. transmitted at controlled environment and at LRT.
 |  |  |  | VR 1.1.4.3 | Conduct link budget computation. | Compute for theoretical losses and gains at every critical points. Measure the losses and gains at every critical points at controlled environment, and at LRT.

## Slide 7: Communication RAS
S/N | System Requirement | S/N | Design Requirements | S/N | Verification Requirements | Verification Method
SR 1.2 | Satellite shall be able to transmit telemetry and mission data to ground station. | DR 1.2.1 | COM MCU shall receive the telemetry data from OBC through UART. |  | Check UART communication between OBC and COMM MCU. | Compare OBC transmit data and COMM MCU received data.
 |  | DR 1.2.2 | Modulation shall be GMSK at 4800 bps data rate. |  | Confirm the output waveform at the TRX. | Use oscilloscope to check the waveform.
 |  | DR 1.2.3 | Frame format shall be AX.25 Protocol. | VR 1.2.3.1 | Determine the packet error. | Send pre-defined data and inspect the received data for errors.
 |  | DR 1.2.4 | Antenna shall be dipole and receives downlink command at 437.375 MHz. | VR 1.2.4.1 | Get the S11 parameter of the antenna. | Use simulation tool (i.e. CST, HFSS). Use VNA at anechoic chamber test.
 |  |  |  | VR 1.2.4.2 | Measure transmitted signal power at the antenna. | Use SA at anechoic chamber test. Use SA at LRT.
 |  |  |  | VR 1.2.4.3 | Conduct downlink success rate test. | Count packets successfully transmitted vs. received at controlled environment and at LRT.
 |  |  |  | VR 1.2.4.4 | Conduct link budget computation. | Compute for theoretical losses and gains at every critical points. Measure the losses and gains at every critical points at controlled environment, and at LRT.

## Slide 8: Communication RAS
S/N | System Requirement | ID | Design Requirements | ID | Verification Requirements | Verification Method
SR 1.3 | Satellite shall be able to send CW beacon. | DR 1.3.1 | CW shall contain housekeeping data. | VR 1.3.1.1 | Check read data. | Check read display data.
SR 1.4 | COMM shall survive space environment. | DR 1.4.1 | COMM shall be able to survive thermal test in the range of -10C to 45C. | VR 1.4.1.1 | Shall confirm the COMM can survive thermal test. | COMM operational test in laboratory.

## Slide 9: Communication Subsystem Schedule

## Slide 10: Antenna Deployment
MDR

## Slide 11: Block Diagram for Antenna Deployment
Antenna Deployment
Function - To achieve the deployment of UHF antenna successfully by using the circuit burner mechanism

## Slide 12
S/N | System requirement | S/N | Design Requirements | S/N | Verification Requirements | Margin | Verification Method
SR 1.1. | The Antenna shall not be deployed before satellite release from ISS | DR 1.1.1 | Antenna shall be securely stored in the satellite | VR 1.1.1.1 | Ensure that the wire holding the antenna shall securely store the antenna |  | Fit to check wire tension
 |  | DR 1.1.2 | Antenna shall not deploy inside JSSOD pod | VR 1.1.2.1 | Antenna shall not deploy during different vibration conditions. |  | Vibration tests
 |  | DR 1.1.3 | Burner Circuit shall not activate within 30 mins after the satellite release from ISS | VR 1.1.3.1 | Measure the time when the burner circuit is activated |  | Long duration test, end to end test, after 30 mins comm test
SR1.2 | Antenna shall be deployed after satellite release from ISS | DR 1.2.1 | Burner circuit will be activated 30 mins after the satellite release from ISS | VR 1.2.1.1 | Measure the time when the burner circuit is activated | +1 min | Functional and deployment test.
 |  | DR 1.2.2 | One Antenna is completely deployed within 20 sec after the burner circuit activated and another antenna is deployed after next 10 mins. | VR 1.2.2.1 | Measure the time when the antenna is completely deployed | +/- 5 sec | Functional and deployment test.
 |  | DR 1.2.3 | EPS shall supply 3.6 to 4.2 V unregulated voltage and 3A current to Burner Circuit | VR 1.2.3.1 | Measure supply voltage and current to the Burner Circuit | 3.6-4.2 V/ 3A | Functional and deployment test.
Antenna Deployment RAS

## Slide 13
Antenna Deployment RAS
ID | System requirement | ID | Design Requirements | ID | Verification Requirements | Verification Method
SR 1.3. | Antenna Deployment system shall be done with design limitations | DR 1.3.1 | Position of antenna and antenna deployment components shall not affect other subsystems operation | VR 1.3.1.1 | Make design simulation of the position of each components | CAD design inspection system functional test
 |  | DR 1.3.2 | Antenna deployment mechanism will not harm the astronaut safety | VR 1.3.1.2 | Check material | Vibration tests
SR 1.4 | Antenna shall be able to receive and transmit from and to ground stations respectively | DR 1.4.1 | Antenna shall be dipole operating at 435 MHz and 437.375 MHz UHF amateur band | VR 1..4..1.1 | Get the S11 parameter of the antenna(ensure antenna length is around 17.2 cm) | Use simulation tool (i.e CST, HFFS) Use Vector Network Analyzer (VNA) at anechoic chamber test
 |  | 1.4.2 | S and F and APRS antenna shall work at 144-146 MHz | 1.4.2.1 | Ensure antenna length is around 51.03 cm | CST Simulation Antenna measurement
 |  |  |  | VR 1.4.2.2 | Measure received signal power at the antenna | Use spectrum analyser (SA) at anechoic chamber test Use SA at Long Range Test (LRT)

## Slide 14
Antenna Deployment RAS
SR 1.5 | Antenna deployment system shall be able to withstand the space environment | DR 1.5.1 | Antenna deployment system shall be able to survive thermal test in the range of -10 Deg Cel to 45 Deg Cel | VR 1.5.1.1 | Shall confirm the antenna deployment system can survive thermal test | Antenna deployment system operational test in laboratory
SR 1.6 | Antenna deployment system shall be able to perform the anechoic chamber test. | DR 1.6.1 | Antenna deployment system shall be able to perform anechoic chamber test. | VR 1.6.1.1 | Shall confirm the antenna deployment system can perform anechoic chamber test. | Antenna deployment system operational test in laboratory

## Slide 15
Schedule